## Slide 1: Part 1 Overview of NGS technologies and platforms

## Slide 2: Terminology
NGS Next Generation Sequencer (or Sequencing)
Sequence read The nucleotide sequence that comes from a single DNA fragment (on a next-generation sequencer)
Read Pair / Mate pair Two reads from both ends of a DNA fragment, read pairs at distance of several 100 bp or several kb (mate pairs)
Adapter Synthetic sequences added to isolated DNA fragments to help in the amplification, sequencing and identification process (ligation)
Multiplexing The mixing of several samples in the sequencing process where sequences can be assigned later on to the correct sample through the use of barcodes (or indices)
Base calling The process in which base identities are inferred from (light) intensity signals

## Slide 3: layout
Sequencing (a short history)
Main NGD sequencing platforms
The Illumina platform
Sequencing strategies

## Slide 4: Sequencing by synthesis
These are the ingredients of many sequencing technologies
Primer
DNA polymerase
dNTPs
ssDNA template

## Slide 6: Sequencing (r)evolution
Stratton, nature 458, 719-724, 2009

## Slide 7: Gel based sequencing
Amplification stops when a Dideoxynucleotide is integrated

## Slide 8: Capillary sequencing

## Slide 9: Massive parallel sequencing = Next Generation Sequencing

## Slide 10: NGS
Denotes the family of sequencing platforms that have in common their high degree of parallelization and massive data generation.
NGS refers to the sequencing techniques that have succeeded Sanger (dideoxy) sequencing
An unlucky name, since a new generation after NGS is already around ( NNGS?)

## Slide 11
What NGS technologies DON’T offer is: targeted, high accuracy sequencing of small regions
What NGS technologies DO offer is: massive data generation of whole genomes, chromosomes, transcriptomes, exomes etc.

## Slide 12: Sequencing technologies: goals
More data for less money
Longer reads!!

## Slide 13: The read length race
Why are longer reads so desirable?

## Slide 14: Why read pairs?
In Paired-end sequencing, both ends of the DNA fragment are sequenced
Because the distance between each paired read is known, alignment algorithms can use this information to map the reads over repetitive regions more precisely.
www.illumina.com

## Slide 15: Read pairs versus Mate pairs
Because larger inserts can pair reads across greater distances, they provide a better ability to read through highly repetitive sequences and regions where large structural rearrangements have occurred
www.illumina.com

## Slide 16: Main NGS sequencing platforms
Single-molecule real-time sequencing
(Pacific Bio)
Ion semiconductor (Ion Torrent sequencing)
Pyrosequencing (454)
Sequencing by synthesis (Illumina)
Sequencing by ligation (SOLiD sequencing)

## Slide 17: Comparison of next-generation sequencing platforms

## Slide 18: Principles of 2nd generation NGS sequencers
Clonal amplification
  Emulsion PCR  Roche / Ion Torrent
  Bridge PCR  Illumina
Sequencing in cycles (Short reads)
  454
  Illumina
  Ion Torrent/Proton

## Slide 19: 454 (Roche), SOLiD and Ion Torrent use Emulsion PCR for amplification

## Slide 20: Roche 454: pyrosequencing
PPi

## Slide 21: Roche 454: pyrosequencing
APS = Adenosine 5’-phosphosulfate

## Slide 22: Roche 454: pyrosequencing
mammoth.psu.edu
The big weakness of 454 sequencing: homopolymers give fast increasing error rate with increasing length
Notes: What are the downstream effects when analyzing a read with (long) homopolymer?

## Slide 23: The Roche 454 homopolymer problem
movie
Notes: Column 1 does not add up to 100%!

## Slide 24: Ion Torrent sequencing
PPi
+H+

## Slide 25: Ion Torrent sequencing
movie

## Slide 26: SOLiD sequencing
Sequencing by ligation
1600 million (!!) reads per run (160 Gb data)
Max 75 bases read length
Does not sequence bases but rather dinucleotidess

## Slide 27: SOLiD sequencing

## Slide 28: SOLiD sequencing

## Slide 29: SOLiD sequencing
movie

## Slide 30: Single molecule sequencers
PacBioRS
Oxford Nanopore
Helicos
  No amplification required for the reads
  Longer Read (excluding Helicos)
  Base modification detection (excluding Helicos)

## Slide 31: Single molecule sequencers - PacBio
2-3 kb single continuous read!
High (>10%) error rate!
movie

## Slide 32: Is a high error rate bad per se?
Not with high coverage
Not with low systematic error rate!
Notes: Coverage for mutation call in Diagnostics department minimum 5 (in Nextgene) and 20 in Cartagenia. Average coverage 300!

## Slide 33: Systematic versus random errors
HiSeq
PacBio

## Slide 34: Single molecule sequencers – Oxford Nanopore
No enzyme
or label!
movie

## Slide 35: Helicos sequencing
Movie

## Slide 37: Single Molecule Sequencing = the future
Nanopores with electrical real-time analysis and without the need for optics, labels, amplification or fluidics looks like the next level of sequencing
But needs
  Increased number of reads per run
  Improved accuracy
  Decreased reagent costs

## Slide 38: Part 2 Overview of NGS technologies and platforms

## Slide 39: The Illumina platform
umcg/genetics

## Slide 40: A sequencer for every need
www.illumina.com

## Slide 41: The stages in Illumina sequencing
Sample preparation & target enrichment
Sequencing
Data processing

## Slide 42: Sample preparation for Illumina
DNA isolation
QC on DNA prep
Fragment/shear DNA
Adapter ligation
Size selection (300-350 bp)
Amplification (=PCR) of selected fragments
QC of amplified material

## Slide 43: DNA processing summary
www.illumina.com
Platform-specific oligonucleotide adapters, needed to perform the sequencing biochemistry and index samples, are ligated to each end of the fragments to yield the sequencing-ready library
Repair and add Adenine overhang
Ligate adapters

## Slide 44: Adapters up close
Elements that can be included in NGS adapters on the Illumina platform.
SP1=primary sequencing primer; SP2=paired-end primer; IP=sequencing primer for the index read.
(A) Minimal adapter components. (B) Barcode configuration supporting a paired-end read. (C) Index configuration supporting a paired-end read.
http://rnaseq.uoregon.edu
Index’s can be used for upfront de-multiplexing

## Slide 45: Optimal Illumina library profiles
Single peak at 340-390 bp (including adapters) with small size distribution
No primers present (peaks < 70 bp)
No empty library present: peak at 125-130 bp

## Slide 46: GIGO: Garbage in, Garbage out
Primer peaks
364 Bp
Ideal situation!

## Slide 47: GIGO: Garbage in, Garbage out
Primer peaks
at 59 & 84 bp
Main peak at 214 bp too short for PE run
Bad situation!
Do not sequence this
Empty library peak at 125 bp

## Slide 48: Targeted sequencing: Capturing of a panel of genes
Input: Prepped Genomic DNA
Custom made library kit (bait)
Hybridization
Magnetic Beads
Capture beads with magnet
Wash and elute beads
Amplify
QC of captured material
Pooling of 12 samples
Notes: There are standard library kits available, such as SureSelect Whole Exome kit

## Slide 49: Target enrichment
www.illumina.com

## Slide 50: Sample pooling
Since one sequencing lane generates so much data, samples are pooled when less reads per sample are required
A sample-specific unique index (barcode) is added in last amplification step
Index: A 6-mer at an edit or Hamming distance of at least 2 (most 3) from any other index sequence to minimize the chance of mix-ups
Notes: Not all indexes (or sequences) should start with the same base, otherwise the camera alignment will be problematic

## Slide 51: Multiplexing using barcodes
www.illumina.com

## Slide 52: The actual sequencing
The sequencing process on Illumina is a sophisticated process of fluidics
DNA templates are attached to a flow cell
All sequencing steps are performed by flowing reagents over the attached DNA

## Slide 53: The sequence of sequencing (1)
Attach DNA to flow cell
Bridge amplification to generate clusters
Denaturing and annealing of sequence primers
Sequencing in 100-150 cycles:
Single DNA-fragments are attached to the flow cell by hybridizing to oligos on its surface that are complementary to the ligated adapters

## Slide 54: The sequence of sequencing (2)
Each of these clusters derives from a single unique DNA fragment
Attach DNA to flow cell
Bridge amplification to generate clusters
Denaturing and annealing of sequence primers
Sequencing in 100-150 cycles
Bridge amplification yields a high-density unordered array of amplified DNA fragments
wikipedia.org
www.illumina.com

## Slide 55: The sequence of sequencing (3)
Annealed sequencing primer
Attach DNA to flow cell
Bridge amplification to generate clusters
Denaturing and annealing of sequence primers
Sequencing in 100-150 cycles
The reverse strands are cleaved and washed away and the sequencing primer is hybridized to the DNA-templates
www.illumina.com

## Slide 56: The sequence of sequencing (4)
Attach DNA to flow cell
Bridge amplification to generate clusters
Denaturing and annealing of sequence primers
Sequencing in 100-150 cycles
A blocked base is attached to the end of the growing chain (or primer), detected by fluorescence and deblocked for the next cycle
www.illumina.com
Each base has its specific fluorescent label

## Slide 57: Illumina sequencing movie
movie

## Slide 58: From image to sequence
The raw product of the sequencing reaction is a time-lapse series of images with fluorescent signals in an unordered grid
Ideal
Theory

## Slide 59: From image to sequence (2)
Practice:
Dust specks
Proximity
Low signal
Noise
Degradation during cycles

## Slide 60: From image to sequence (3)
The time-lapse series of images is transformed into a textual representation of nucleotides and the probability of false identity for each nucleotide
We call this process base calling
@HWI-962:64:D0BNFACXX:7:1101:1227:2119 1:N:0:GATCAG
TGCTACGAT
+
CCCFFFII9
@HWI-962:64:D0BNFACXX:7:1101:1176:2147 1:N:0:GATCAG
TTTTTTTGT
+
CCCFFFFFG
Sequence 1
Quality of sequence 1

## Slide 61: Minimize technical variance through randomization
Avoid bias: don't order your samples in a logical way !!!
Example for 2 groups with 4 samples each
Notes: In practice at Diagnostics dept 12 patient samples from same group

## Slide 62: Part 3 Overview of NGS technologies and platforms

## Slide 63: Sequencing strategies
De novo genomic sequencing
Genomic resequencing
  Whole-genome
  Target enrichment (exome, gene panel)
Metagenome sequencing
RNA-seq
ChIP-seq
Small RNA (miRNA) sequencing
etc

## Slide 64: Pros and cons of targeted sequencing
PROS
Cheaper (while capturing cost < sequencing cost)
Higher coverage
Decreased risk of unsolicited findings
Less variants to analyze

## Slide 65: Pros and cons of targeted sequencing
CONS
New gene is discovered  new target set  validation etc + resequencing
You cannot identify new genes or pathways
The capture may introduce (strand) bias
The true variant may be outside the region analyzed (e.g. intronic, UTR)
As sequencing gets cheaper the capture method may become too expensive

## Slide 66: Structural Variants and their detection
http://compbio.cs.brown.edu/projects/structvar/

## Slide 67: Structural Variants and their detection: deletion & insertion
http://www.nature.com/nrg/journal/v12/n5/images/nrg2958-f2.jpg

## Slide 68: Sequencing strategies: RNA-seq
RNA-seq / cDNA sequencing is done to get insight into
gene expression levels
different allele expression
alternative splicing
(alternative) transcription start sites (deepCAGE)
(alternative) polyA site mapping (deepSAGE)
Translation start site identification (Ribosome Profiling / RPF)
(anti)sense expression
Etc

## Slide 69: Techniques for expression profiling
A few genes
Northern blot
Quantitative RT-PCR
Genome-wide
Microarrays
RNA-seq
miRNA-seq

## Slide 70: RNA-seq (Illumina)
Geospiza.com, edited

## Slide 71: Example of RNA-seq (Illumina)
Geospiza.com, edited

## Slide 72: ChIP-seq
Chromatin ImmunoPrecipitation
  Investigate Protein-DNA interactions

## Slide 73: ChIP-seq: study of Transcription Factors
TFs are modular proteins that recognize specific DNA motifs
TFs regulate gene expression, and consequently many important cellular processes
TFs are often mutated or aberrantly expressed in human disease

## Slide 74: ChIP-seq overview
wikipedia.org
Using Formaldehyde

## Slide 76: ChIP-seq visualization
Find peaks  Peak is binding site of protein

## Slide 77: ChIP-seq
Pros:
  Protein-DNA interactions are detected as they occur in vivo
  Quantitative (qPCR analysis)
  Adaptable to genome-wide analysis
  Can be performed for all proteins recruited to the DNA
Cons:
  Requires suitable antibodies
  Extremely inefficient (0.001-0.1% of input is recovered)
  Low-affinity binding events are easily missed (antibody dependent)
  Not a functional experiment on its own